## Slide 1: Communication Protocols in IoT
Overview

## Slide 2: Communication we come across in IoT
For any two devices to communicate with each other we need a connectivity
The connectivity to the network could be wired or wireless
There three types of Networking seen in IoT
Thing-to-Proxy
Thing-to-Things
02
01
03
Thing-to-Internet

## Slide 3: Thing-to-Things
In Thing-to-Things Networking, one thing communicates with other thing/things by sending messages, commands or data
Example: Thing-to-Things communication is seen in RFID Technology

## Slide 4: RFID Tag
The RFID tag has an embedded transmitter and receiver. The actual RFID component contained in a tag has two parts:
An integrated circuit for storing and processing information, and an antenna to receive and transmit a signal
The RFID tag has non-volatile memory storage, and can included either fixed or programmable logic for processing transmission and sensor data
A basic RFID system comprises two parts: the Tag, and the Reader.
Tag
1

## Slide 5: RFID Tag
A Passive Tag is the cheapest option, and features no battery. The tag uses radio energy transmitted by the reader
An Active Tag features an onboard battery, periodically transmitting its credentials
A Battery-Assistive Passive Tag also features a small onboard battery, but is only activated when in the presence of an RFID reader
Furthermore, a tag may be either read-only, or read/write. A read-only tag has a factory assigned serial number used for identification in a database, while a read/write tag can have specific custom data written to the tag by the user
Tags can be passive, active, or battery-assistive passive
Tag
1

## Slide 6: RFID Working
In most of the RFID system, tags are attached to all items that are to be tracked. These tags are made from a tiny tag-chip that is connected to an antenna.

## Slide 7: Thing-to-Proxy
In Thing-to-Proxy Networking, one thing communicates with other thing/things by sending messages, commands or data via Proxy/Hub
In this case, switch is sending a command to bulb

## Slide 8: Thing-to-Proxy
Thing-to-Proxy communication can happen with Bluetooth, WIFI, ZigBee etc. via Hub
Via Hub

## Slide 9: Thing-to-Proxy Networking : Example
Below are few examples for Thing-to-Things Networking:
Bluetooth
WIFI
ZigBee

## Slide 10: Things-to-Internet
Things-to-Internet connection can be a direct connection or via proxy

## Slide 11: Things-to-Internet
Things-to-Internet connection can be a direct connection or via proxy
Direct connection to internet with LAN or WIFI
Connection to internet via Proxy (i.e. RaspberryPi)

## Slide 12: IoT Communication Requirements
Battery life
High-bandwidth
Security
Time
Therefore, it is crucial to choose the best IoT connectivity option for your specific needs
Let us discuss the major ways in which IoT devices connect to Internet

## Slide 13: IoT Wireless Connectivity
IoT devices mostly connect to internet Wirelessly
Based on the range of coverage , Wireless IoT Technologies are classified as:

## Slide 14: Wireless IoT Networking: Short Range
Bluetooth
WIFI
ZigBee
6LoWPAN
In short range, we will discuss the below networks, which are widely in use:

## Slide 15: BLE Use Case: iBeacon (Protocol Developed by Apple)
iBeacon is based on Bluetooth Low Energy proximity sensing by transmitting a universally unique identifier picked up by a compatible app or Operating System
iBeacon can be used to determine the device's physical location, track customers, or trigger a location-based action on the device such as a check-in on social media or a push notification

## Slide 16: BLE Use Case: iBeacon (Protocol Developed by Apple)
Use Case: Problem
01
02
South Korea is eagerly encouraging its residents to have larger families given that the country’s birth-rate is one of the lowest birth-rates in the world
A beacon campaign called the “Pink Light Campaign” is being trailed on subways in the city of Busan, South Korea
To combat the risk of miscarriage for pregnant women by offering priority seating on public transport for them via beacons
Use Case: Solution

## Slide 17: BLE Use Case: iBeacon (Protocol Developed by Apple)
1
3
4
First beacon is attached to bag or any accessory of pregnant women
The second is the light sign that is installed on trains. As soon as a pregnant woman gets on board, the beacon she is carrying signals the light to flash
The blinking of the pink sensor lets people know that a pregnant lady is aboard and will need a vacant seat. Especially alerts other passengers who might be sitting in the courtesy seat
Once the system detects that the woman is seated, the light switches off
The system aims to make public transportation easier for pregnant women
2
5

## Slide 18: Wireless IoT Networking: Long Range
In long range wireless IoT Networking, let us discuss:
Cellular
LPWAN
Cellular
LPWAN

## Slide 19: Connecting to Internet
Ethernet (built-in), plug it in anywhere
Wi-Fi (built_in), configured once per location
3G (dongle), configured once, easy to use

## Slide 20: Connection Protocols
IP Enabled Connection
  LAN
  Wifi
  3G / 4G
Wired Connection (RS232 / RS485)
Wireless Connection
  Bluetooth
  Zigbee
  LoRaWan

## Slide 21: Protocols Used
HTTP Requests
REST (REpresentational State Transfer)
MQTT (Message Queue Telemetry Transport)
DDS
AMQP
JMS
CoAP
Many more

## Slide 22: REST

## Slide 23: Application layer IoT Network Technologies
HTTP and HTTPS are ubiquitous across internet applications, which is true also within IoT, with RESTful HTTP and HTTPS interfaces widely deployed
Client
Server
Request
Response
Get
Post
[{“city”: “Bangalore”, “price”: “rupees”}]
[{“low”: “2500”, “high”: “5500”}]
/flight/availability

## Slide 24: MQTT
Publish
Subscribe
These properties make MQTT perfect solution for Internet of Things applications
MQTT is a lightweight publish and subscribe system, where you can publish and receive messages as a client, it runs on top of TCP
It is a simple communication between multiple devices and simple messaging protocol for
Constrained Devices
Low Bandwidth

## Slide 25: MQTT

## Slide 26: What does MQTT allow?
Here's a quick overview of what MQTT allows you to do:
Send a command to control an output
Read data from a sensor and publish it
or
MQTT
MQTT
MQTT
MQTT
Sensor
RaspberryPi
A programming language
Light

## Slide 27: Concepts of MQTT
In MQTT, there are few basic concepts which you need to understand:
Publish / Subscribe
Messages
Topics
Broker

## Slide 28: MQTT: Broker
The broker is primarily responsible for:
Receiving all messages
Filtering the messages
Deciding who is interested in topic and then publishing the message to all subscribed clients
Device 1
Device 2
Publish
Publish
Subscribe
Broker

## Slide 29: Thank you